## Slide 1
w
START
Define Design Specifications
Select device type: Double Gate MOSFET
Choose technology node (e.g. 20 nm / 32 nm)
Define channel and gate dimensions
Set oxide thickness range / dielectric materials (e.g. SiO2, HfO2)
Develop Device Geometry using SDE Tool
(Structure Design Editor)
Create 2D/3D Double Gate MOSFET structure
Define source, drain, channel, gates, dielectrics
Generate proper meshing
Apply Required / Suitable Physics Models (SDevice Tool)
Select drift-diffusion, mobility, recombination models
Define material / electrical properties, boundary conditions
Run Simulation & Analyze Device Characteristics (SVisual Tool)
Id vs Vg, Id vs Vd plots
Threshold voltage, ON/OFF current, leakage current
Compare graphs for various dielectric cases
Check If Design Meets Performance Targets
① Is Ion high enough?
② Is Ioff low enough?
③ Is VIN within acceptable range?
④ Is short-channel effect minimized?
NO
YES
Conclude the Work
Identify best dielectric material
Identify optimum thickness
Summarize improvements achieved
Suggest future enhancements
END
Double Gate MOSFET Simulation — Design Flow